 struct memblock_region {
     phys_addr_t base;
     phys_addr_t size;
 };
 struct memblock_type {
     unsigned long cnt; /* number of regions */
     unsigned long max; /* size of the allocated array */
     phys_addr_t total_size; /* size of all regions */
     struct memblock_region *regions;
 };
 struct memblock {
     phys_addr_t current_limit;
     struct memblock_type memory;
     struct memblock_type reserved;
 };
#define INIT_MEMBLOCK_REGIONS 128
#define MEMBLOCK_ALLOC_ANYWHERE (~(phys_addr_t)0)
struct memblock_region memblock_memory_init_regions[128];
struct memblock_region memblock_reserved_init_regions[128];
struct memblock memblock = {
        .memory.regions = memblock_memory_init_regions,
        .memory.cnt = 1, /* empty dummy entry */
        .memory.max = INIT_MEMBLOCK_REGIONS,
        .reserved.regions = memblock_reserved_init_regions,
        .reserved.cnt = 1, /* empty dummy entry */
        .reserved.max = INIT_MEMBLOCK_REGIONS,
        .current_limit = MEMBLOCK_ALLOC_ANYWHERE,
};
memory.cnt = 1
memory.max = 128
memory.total_size
[0]
phys_addr_t base;
phys_addr_t size;
[1]
...
[127]
memory.cnt = 1
memory.max = 128
memory.total_size
...
[127]
current_limit = !0

---
  void bootmem_init(void);
void find_limits(unsigned long *min, unsigned long *max_low, unsigned long *max_high);
void arm_bootmem_init(unsigned long start_pfn, unsigned long end_pfn);
void arm_memory_present(void)
void sparse_init(void)
void arm_bootmem_free(unsigned long min, unsigned long max_low, unsigned long max_high);
▶ arm_bootmem_init() 함수
- struct memblock memblock 구조체의 memory, reserved 멤버를 초기화
- reserved 멤버를 초기화
【〔int memblock_reserve(phys_addr_t base, phys_addr_t size);〕】
- memory 멤버 초기화
【〔int memblock_add(phys_addr_t base, phys_addr_t size);〕】
- memblock 구조체의 memory와 reserved 멤버를 초기화는 공통 함수
  (memblock_reserve(), memblock_add() 함수 내부에서 호출)
【〔mm/memblock.c-int memblock_add_region(struct memblock_type *type, phys_addr_t base, phys_addr_t size, int nid);〕】

---
base
base
base
base
base
base
base

---
- PFN은 메모리를 4KB 크기로 나누었을 때
 각 각의 고유한 블록의 구분 번호
- 메모리를 나었을 때 2개 또는 그 이상에
걸쳐 메모리가 나누어 질 수 있음을 주황색
 선으로 표시함
- 구조체 meminfo의 bank 멤버의
0번 인덱스를 'min', high memory를
'max_high', 이 전을 'max_low'로 지칭
memory.cnt = 1
high memory
memory.max = 128
memory.total_size
phys_addr_t start;
Int highmem;
phys_addr_t start;
Int highmem;
...
min
[127]
[2]
phys_addr_t start;
Int highmem;
PFN[0]
memory.cnt = 1
PFN[1]
[3]
phys_addr_t start;
Int highmem;
start
memory.max = 128
[4]
phys_addr_t start;
Int highmem;
end
memory.total_size
[5]
phys_addr_t start;
Int highmem;
max_low
[6]
phys_addr_t start;
Int highmem;
...
max_high
PFN[n]
[7]
phys_addr_t start;
Int highmem;
[127]
Int nr_banks;
current_limit = !0
struct meminfo

---
phys_addr_t start;
Int highmem;
// min 부터 max_low까지의 pfn 개수를 구함
zone_size[ZONE_NORMAL/*0*/] = max_low – min;
// high memory부터 max_high까지의 pfn 개수
zone_size[ZONE_HIGHMEM/*1*/] = max_high – max_low;
if (start < max_low) {
    unsigned long low_end = min(end, max_low);
    // max_low 전까지 pfn 개수를 뺌
    zhole_size[0] -= low_end – start;
}
if (end > max_low) {
    unsigned long high_start = max(start, max_low);
    // ?
    zhole_size[ZONE_HIGHMEM] -= end - high_start;
}
phys_addr_t start;
Int highmem;
[2]
phys_addr_t start;
Int highmem;
[3]
phys_addr_t start;
Int highmem;
zone_normal
[4]
phys_addr_t start;
Int highmem;
[5]
phys_addr_t start;
Int highmem;
zone_high
[6]
phys_addr_t start;
Int highmem;
[7]
phys_addr_t start;
Int highmem;
Int nr_banks;
struct meminfo
zone_normal
zhole_size[0]에는 max_low부터 end까지의 pfn 개수
zone_high

---
size = zones_size[j]
realsize = freesize = size – zholes_size[j];
calc_memmap_size(zones_size[j], (size – zholes_size[j]));
-----------------------------------------------------------------------
unsigned long calc_memmap_size(unsigned long spanned_pages, unsigned long present_pages)
{
    unsigned long pages = spanned_pages;
    if (zones_size[j] > ((size - zholes_size[j]) + ((size - zholes_size[j]) >> 4))
        pages = present_pages;
    return PAGE_ALIGN(pages * sizeof(struct page)) >> PAGE_SHIFT;
}
zone_normal
zhole_size[0]에는 max_low부터 end까지의 pfn 개수
zone_high
[Speaker Notes: /* * Provide a more accurate estimation if there are holes within * the zone and SPARSEMEM is in use. If there are holes within the * zone, each populated memory region may cost us one or two extra * memmap pages due to alignment because memmap pages for each * populated regions may not naturally algined on page boundary. * So the (present_pages >> 4) heuristic is a tradeoff for that. */]